## Slide 1: FPGA-Based Prototyping Part 2
Victor Grimblatt
SPL – 2011

## Slide 2: FPGA Resources Types
Resource | Utility for Prototyping | Inferred?
Logic blocks | Very high, the essential building block | Always
RAM blocks | High major building block | Usually
DSP blocks | High, majhor building block | Usually (some IP instantiation)
Clock generation | Very high, an essential but limited resource | Often (may need RTL change)
Clock distribution | Very high, global nets are precious resource | Usually
General IO | Very high, an essential and precious resource | Always (type set by attribute)

## Slide 3: FPGA Resources Types
Resource | Utility for Prototyping | Inferred?
Fast serial IO | High, useful for prototyping standard IP blocks | Seldom (requires IP instantiation)
Hard IP | Very powerful block but utility is design dependent | Never (requires IP instantiation)
System Monitor | High, will protect investment in FPGA hardware | Never (requires design in)

## Slide 4
SoC RTL project
Design synthesis
Partitioning
FPGA adaptation
Constraint
Design synthesis
Place & route
Device programming
Behavioral simulation
Functional simulation
Timing simulation
Static timing analysis
In-circuit verification
Design Verification

## Slide 5: FPGA-Based Prototyping Process Overview
Synthesis
Design adaptation for FPGA
Partitioning
Constraint generation
Place & route

## Slide 6: Synthesis
May be performed before of after partitioning
Convert RTL into an FPGA netlist
Generates an FPGA netlist for the chosen device and the implementation constraints
Provides early estimation of the expected performance

## Slide 7: Design Adaptation for FPGA
SoC RTL is modified to better fit the FPGA technology and the specific prototyping platform
Typical modifications
Removes blocks not to be prototyped
Replaces SoC-specific structures with FPGA structures like clock generation and other IP
Resizes blocks (e.g. memories) to better fit in FPGA

## Slide 8: Partitioning
FPGA-ready version of the SoC RTL design is divided into blocks that map into individual FPGAs
Needed for designs that do not fit into a single FPGA
Can be done manually or using partitioning tools

## Slide 9: Constraint Generation
Convenient point to enter implementation constraints such as timing and pin placements
Constraints may be generated and applied to back-end tools, however doing that before synthesis generates a better netlist
Can meet area/speed constraints after place & route

## Slide 10: Place & Route
Converts the FPGA netlist and the user constraints into an FPGA bit stream
Bit stream will be loaded into the FPGA to provide it with the design functionality
Involves a number of steps
Mapping
Place & route
Timing analysis